Security door
using RFID
product
Specification.

1
# Product requirements
To show the product requirement in term of
Overall product description
H/W requirements Ex. Need SD card, LAN
S/W requirements Ex. Need support TCP/IP, IR protocal
User interface requirement ex. Graphic, text
Packaging requirement Ex. Size, Material
Product concepts
Door control system by using RFID technology to Identity user for allow or disallow user to go in building.
Thai
Product description
- สามารถตรวจสอบได้ว่ามี RFID card ที่นำมา stamp เหมือนหรือต่างกับ ข้อมูล RFID card ที่เก็บอยู่
- สามารถเก็บ รหัส RFID card เข้าสู่ระบบได้
- สามารถลบ รหัส RFID card ออกจากระบบได้
- สามารถเก็บเวลาที่มีการนำ RFID card มาทำการ stampได้
- สามารถใช้ RFID เชื่อมต่อแบบ Wiegand interface ได้
- Display section
- password without RFID
H/W requirements (SYSTEM REQUIREMENT FEATURES)
No	Requirements
HW-1	Use ARM7 as the core development
HW-2	Support Wiegand interface for LF 125 MHZ and MF (13.5 Mhz)
HW-3	Use keypad for the input
HW-4	Interface to 220 V device for control doors
HW-5	Menu select on LCD for operation
HW-6	Can save data in SD card
HW-7	Can save time when power off and on again

S/W requirements
No	Requirements
SW-1	Input password and control using keypad
SW-2	Read and compare RFID card with the Database
SW-3	Add , Delete RFID Card from the database
SW-4	Output control to relay to control 220 V device
SW-5	Can show graphic icons
SW-6	Can show character in text mode
SW-7	Menu driven interface
SW-8	Read /Write data to SD card
SW-9	Can save time
SW-10	Can set time

2
# Module Partition
This chapter partition project into block. Both HW block and SW block an check whether block available or need to new design or expand current block. (Use to show for who do what and task done)
E-block Software for ARM module
Need SW Module	Available	Create new
Keypad (change map to module namein SW SPEC)	No	Yes
Time	No	Yes
SPI	No	Yes
LCD	No	Yes
RFID	No	Yes
Relay	No	Yes
SD/MMC reader	No	Yes

E-block Hardware module
Need HW block	Available	Create new
ARM7 LPC2138	Yes	No
Keypad	Yes	No
G LCD	No	Yes
Wiegand RFID reader	No	Yes
SD/MMC reader	No	Yes
Relay	Yes	No

E-block Hardware module requirement
HW block	Need Features	Requirement Mapping
E_ARM7	E_ARM 7 ( E-block CPU using ARM7 LPC2138) / Map to E-block pin / Serial port and JTAG port to program	HW-1
E_RFID	E_RFIDWiegand RFID (125 kHz) / Output in Wiegand interface / Regulate V from 12 V ( Reduce power supply)	HW-2
E_MATRIX	E_MATRIX Key pad 12 key (4 x 3) / Support 12 key press / IO need (??) for Rows and column	HW-3
E_Relay	E_Relay ( ส่วนจำลอง การควบคุม เปิด-ปิด ประตู )	HW-4
E_GLCD	E_GLCD ( ET-NOKIA LCD 5110 ) / Backlight for LCD / SPI interface	HW-5
E_SD/MMC	E_SD/MMC Reader (ET-MINI SD/MMC) / SPI interface / SD/MMC socket / Write protect / Card detect ?	HW-6

E-block Software module requirement
SW block	Need Features	Requirement Mapping
E_ARM7_Keypad	Keypad Controller / - Can get pressed key from keypad ( How many keys)	SW-1
E_ARM7_RFID	- RFID Reader Controller / - Can get data from RFID card	SW-2
Relay	Relay Controller / - Can receive input and simulate door open	SW-4
GLCD	Graphic LCD Controller / - Can show picture / - Can convert character to show on LCD	SW-5 / SW-6 / SW-7
SD/MMC reader	-SD/MMC Reader controller / Can load data / Can save data	SW-8
E_ARM7	- Interface with SD and GLCD via SPI / - Save /Set time using RTC / Read RFID using interrupt	SW-9 / SW-10

3
# Module Integration
This chapter explain how to do module integration both H/W and S/W module

H/W integration
S/W integration
ตรวจสอบว่าอยู่ใน
state delete หรือไม่
ตรวจสอบว่ามีการ
กด key * หรือไม่
เริ่มต้นการทำงาน โดยทำการ initial ระบบทั้งหมด
ทำการรับข้อมูลจาก keypad
แล้วก็เปลี่ยน password
ตรวจสอบว่าอยู่ใน state
delete password หรือไม่
ตรวจสอบว่าอยู่ใน state
add password หรือไม่
ตรวจสอบว่าอยู่ใน state
change password หรือไม่
ทำการรับข้อมูลจาก keypad
แล้วก็ลบ password user
ทำการรับข้อมูลจาก keypad
แล้วก็เพิ่ม password user
ทำการรับข้อมูลจาก keypad
แล้วก็เปลี่ยนวันที่และเวลา
ตรวจสอบว่ามีการ
กด key ตัวเลข หรือไม่
ตรวจสอบว่าอยู่ใน
state set time หรือไม่
ตรวจสอบว่าอยู่ใน
state compare หรือไม่
ตรวจสอบว่าอยู่ใน
state save หรือไม่

เปลี่ยน state เป็น config
เปลี่ยน state เป็น config

ตรวจสอบว่า มีการ
stamp card รึป่าว
เก็บข้อมูลลง
SD/MMC card

เก็บข้อมูลลง
SD/MMC card

Yes

No

Yes
Yes

Yes

Yes
No

Yes
No
No

ทำการเก็บข้อมูล card

Yes

Yes
No

ทำการลบข้อมูล card

No

ตรวจสอบว่าอยู่ใน state
config หรือไม่
ทำการรับข้อมูลจาก keypad
แล้วเปลี่ยน state ตามหมายเลข
ตรวจสอบว่ามี password
user นี้ในระบบหรือไม่

ทำการรับข้อมูลจาก keypad
Yes

ประตูเปิด 5 วินาที

Yes
Yes
Yes
Yes
No
No
No
No
No
No
ตรวจสอบว่ามี card
นี้ในระบบหรือไม่
4
# Testing
Testing environment
Specify testing environment use in this project
There are tests for module and integration test for whole project.
Module testing refer to each module testing work sheet.
Integration testing map by translate requirement to test case, specify test expectation and test results

From requirement table map to test case

Requirement	Test cases	Expect results	Results
HW-1	1.1 Load program into E_ARM / 1.2 Run program from E_ARM	Load and run program properly
HW-2
HW-3
HW-4
HW-5
HW-6
HW-7
SW-1
SW-2
SW-3
SW-4
SW-5
SW-6
SW-7
SW-8
SW-9
SW-10

5
# Wrap up
This chapter is check list for project wrap up to make sure that all documents and files had been updated properly

Tasks	Status
Update E_Block_HWSpec
Update E_Block_SWSpec
Project document
Put all source code in repository
Put all schematics in repository
Put all PCB in repository
Update Web and E-block catalog
Provide bug report form