Bootloader for E-block's Specification

1. Load by using terminal Emulator send text file in HEX format
2. Support Fusing bits ( Hows)
3. Program EEPROM Data
4. Resident in Bootloader area
5. Enter boot mode “ Press two switched while reset”
6. Check application ID before goto Application section
7. Support XON/XOFF protocol

Program Flow

------------------ Installation -------------------
by Martin Thomas and Preston Manwaring

- Change the MCU type in the makefile. If your
  processor is not listed, modify the makefile
  according to the processor manual.

- Change the boot(loader)-size in main.c, this
  bootloader is larger than 512 words (1024 bytes),
  so select at least _B1024!

- Change the UART constants in sercom.h to match
  your MCU speed and the listed baud rate. As this
  version is not buffered, a slower baud rate is
  required.

- Change the start-condition in main.c. Default
  is: enter bootloader if Pin A7 is connected to
  GND during reset/startup

- Edit the value MT_BOOTLOADER_ADDRESS in the
  makefile according to the selected bootloader
  size. Keep in mind that this value has to be
  given in bytes (not words) in the linker options.

  i.e. ATMega16, boot-size 1024 words, see
  datasheet and find "Boot Reset Adress" for
  "Boot Size" 1024 words is 1C00. 1C00 is given
  in words, so set MT_BOOTLOADER_ADDRESS to
  3800 (=2*1C00)

- Please use at least avr-gcc 3.3.1/avr-libc 1.0
  or WINAVR Sept. 2003 or later to compile and link
  the bootloader.

- upload the hex-File to the AVR (STK500, STK200, SP12
  etc.)

- program the "Boot Flash section size" (BOOTSZ fuses)
  according to the boot-size selected in main.c
  i.e. BOOTSZ=00 for boot-size 1024 words on ATmega16

- enable the BOOT Reset Vector (BOOTTRST=0)

- Set the lock bits to protect the bootloader from
  SPM-writes (Boot Loader Protection Mode 2 in STK500-
  plugin)

- Connect the AVR UART Pins via level-shifter/inverter
  (i.e. MAX232) to you PCs Com-Port.

- Reset the AVR while fullfilling the bootloader start-
  condition. Which means connect PA7 to GND in the default
  config during reste/power-cycle. Keep the connection
  or hold the key down until you see the AVRPROG dialog!

- Start AVRPROG (AVRStudio/Tools or stand-alone) -
  keep PA7 grounded!

- AVRPROG will detect the bootloader, you may release
  PA7 now

- see AVRStudio online-help for more information how
  to use AVRPROG

- make sure to EXIT from AVRPROG (button) to start
  your main-application (or toogle power/reset)

Knowledge Capture

 1) Specify bootloader area by setting fuse bit and parameter in make file ( 1024 ,2048 Bytes)

Fuse	BOOTSZ1 BOOTSZ0

Common pitfalls Value in table BOOTSZx is in Word You need to convert to bytes (multiply by 2) to use in Makefile
ex. 0x3800x 2 = 0x7000 for ATMEGA32 2048 BLS

  2) Select bootloader's size in main program
  3) Move interrupt vector to BLS (Boot Loader Section)

Compile Bootloader
Program bootloader in BLS (Boot Loader Section) Setting parameter in Makefile
 LDFLAG

Configurations
Serial Terminal
- Set serial terminal not to append line feed at the end of lines for ASCII Receiving
- Disable send line end at line feed for ASCII sending

Technical Notes

Issue
    - Cannot download big program
    - Cannot download high speed

Question

Can update bootloader via bootloader ?