Bootloader for E-block's Specification

1. Load by using terminal Emulator send text file in HEX format x
2. Support Fusing bits ( Hows) (Maybe can't do)
3. Program EEPROM Data
4. Resident in Bootloader area x
5. Enter boot mode “ Press two switched while reset”
6. Check Reset vector table before goto Application section x
7. Support XON/XOFF protocol x

Program Flow

# Bootloader program Modification

1) Change the MCU in Makefile Ex MCU = atmega32

2) Specify bootloader area by setting fuse bit and parameter in Makefile ( 1024 ,2048 Bytes). See
  datasheet and find "Boot Reset Adress" for "Boot Size"
Ex MT_BOOTLOADER_ADDRESS = 3800 (=2*1C00) ( For 1024 Bootloader size )
Common pitfalls Value in table BOOTSZx is in Word You need to convert to bytes (multiply by 2) to use in Makefile
ex. 0x3800x 2 = 0x7000 for ATMEGA32 2048 BLS

 3) Select bootloader's size in main program Ex #define _B2048
 4) Move interrupt vector to BLS (Boot Loader Section) By setting GICR bit in main program
   GICR = _BV(IVCE);
GICR = _BV(IVSEL);
**** move Interrupt Vectors to the Boot sector ** WRITE 0 TO IVCE while setting IVSEL
        Use = Not | spend one day to solve this problem !!!
5)Compile Bootloader
Program bootloader in BLS (Boot Loader Section) Setting parameter in Makefile
 LDFLAG

6) Program Fuse bit to select bootloader's size BOOTSZ0, BOOTSZ1 and BOOTRST fuse bit for program to start at bootloader when pressing reset button ( Need to reprogram everytime when update bootloader firmware
Ex 2048 Bytes Bootloader Mark BOOTSZ0 and BOOTSZ1

7) Set the lock bits to protect the bootloader from SPM-writes

# Configurations
Serial Terminal
- Set speed 38400 Non-parity, 1 Stop bit, 8 Data bits and protocol to XON/XOFF
- Set serial terminal not to append line feed at the end of lines for ASCII Receiving
- Disable send line end at line feed for ASCII sending

Technical Notes

# Intel Hex Format

 : 10 7000 00 0C 94 2A 38 0C 94 45 38 0C 94 45 38 0C 94 45 38 27
 : 04 0000 03 00 00 70 00 89
 : 00 0000 01 FF
(1) (2) (3) (4) ----------------------- (5) --------------------------------- (6)

(1) Record Mark Always = ':'
(2) Record Length n Bytes
(3) Offset Address to write
(4) Record Type
        00 Data Record
        01 End of File Record
        02 Extend Segment Address Record
        03 Start Segment Address Record
        04 Extended Linear Address Record
        05 Start Linear Address Record
(5) Data n Bytes
(6) Check SUM ( SUM all Bytes include Check SUM = XX00)

Issue
    - Cannot download big program Solve with XON/XOFF protocol
    - Cannot download high speed Solve with XON/XOFF protocol

Question

Can update bootloader via bootloader ?