Bootloader for E-block's Specification

1. Load by using terminal Emulator send text file in HEX format
2. Program EEPROM Data
3. Resident in Bootloader 2048 Bytes ( Program = 15XX)
4. Enter boot mode “ Press two switched while reset”
5. Check Application's Interrupt vector table before goto Application section
6. Support XON/XOFF protocol at 384000 b/s

Program Flow

# Bootloader Usage
- To enter boot mode, Press reset while pressing SW1, SW2 or both. Display will show b for boot mode
- Press P to program Flash , E to program EEPROM and x to execute program
- If there is program installed ( Check from Interrupt vector table not equal 0xFF) The program will run after press reset
- When prompt for file, send data file (Intel hex format) using sent text files command. The display will show 'P' for program Flash and 'E' for program data into EEPROM when finished, The application program will be run.
# Bootloader program Modification for Other CPU

1) Change the MCU in Makefile Ex MCU = atmega32

2) Specify bootloader 's size by setting fuse bit and parameter in Makefile ( 1024 ,2048 Bytes). See
  datasheet and find "Boot Reset Address" for "Boot Size" In Makefile, search for LDFLAG
Ex MT_BOOTLOADER_ADDRESS = 3800 (=2*1C00) ( For 1024 Bootloader size )
Common pitfalls Value in table BOOTSZx is in Word You need to convert to bytes (multiply by 2) to use in Makefile
ex. 0x3800x 2 = 0x7000 for ATMEGA32

 3) Select bootloader's size in main bootloader program Ex #define _B2048
 4) Move interrupt vector to BLS (Boot Loader Section) By setting GICR bit in main program
   GICR = _BV(IVCE);
GICR = _BV(IVSEL);
**** move Interrupt Vectors to the Boot sector ** WRITE 0 TO IVCE while setting IVSEL
        Use = Not | spend one day to solve this problem !!! Some bootloader use MCUCR don't know why but it's wrong.
5)Compile and Load Bootloader

6) Program Fuse bit to select bootloader's size BOOTSZ0, BOOTSZ1 and BOOTRST fuse bit for program to start at bootloader when pressing reset button ( Need to reprogram everytime when update bootloader firmware
Ex 2048 Bytes Bootloader Mark BOOTSZ0 and BOOTSZ1 and BOOTRST

7) Set the lock bits to protect the bootloader from SPM-writes

# Configurations
Serial Terminal
Set speed 38400 Non-parity, 1 Stop bit, 8 Data bits and protocol to XON/XOFF

# Intel Hex Format

 : 10 7000 00 0C 94 2A 38 0C 94 45 38 0C 94 45 38 0C 94 45 38 27
 : 04 0000 03 00 00 70 00 89
 : 00 0000 01 FF
(1) (2) (3) (4) ----------------------- (5) --------------------------------- (6)

(1) Record Mark Always = ':'
(2) Record Length n Bytes
(3) Offset Address to write
(4) Record Type
        00 Data Record
        01 End of File Record
        02 Extend Segment Address Record
        03 Start Segment Address Record
        04 Extended Linear Address Record
        05 Start Linear Address Record
(5) Data n Bytes
(6) Check SUM ( SUM all Bytes include Check SUM = XX00)

Issue
    - Cannot download big program Solve with XON/XOFF protocol
    - Cannot download high speed Solve with XON/XOFF protocol

# Future Enhancment
- Addresses in intel hex file have not been used. Program had been written at default address for EEPROM and Bootloader.
- When loading end. Cannot show finished message. The program jump to Application directly ??
- Implement watchdog, error handling for power drop
- More support Rectype in intel hex format ( Is it necessary)
- When print * until EOL print new line