E-block
S/W
Module Spec
Template.

Vsion	Date	By	Modified
	10/03/2549	Wichai

0
# Guidelines for the template
Use this template to document the new software template. Chapter 1 is the index for all SW Module Start from chapter 2 is each SW module spec which compose of the following items. Appendix A is the chapter template. To use template just copy Appendix A to your new chapter. And fill in the template. All Software should using doxygen for generate the documents from source code.

- Module Objective
- Function API Description
- Theory of operation for this module
- For input/ output see detail in doxygen document
- State Diagram
- State Transition Matrix
- Flow chart
- Future expansion (if any)
1
# SW Module catalog
This chapter collects all the SW modules which had been developed.
E-block Software module
SW Module	HW Module
io_7segment.c,.h	E_IO
io_piezo.c,.h	E_IO
io_sw.c,.h	E_IO
io_ir.c,.h	E_IO
avr32_uart,.h	E_Mega32
avr32_i2c,.h	E_Mega32
avr32_eeprom,.h	E_Mega32
Avr32_adc.c,.h	E_Mega32
avr32_spi.c,.h	E_Mega32
avr32_tcp.c, .h	E_Mega32
avr32_ip.c, .h	E_Mega32
avr32_udp.c,.h	E_Mega32
avr32_http.c, .h	E_Mega32
enc28J_mac.c,.h	E_enc28J
sd_main.c. ,h	E_sd
sd_fat.c. .h	E_sd
camera_main.c,,h	E_camera

 2
# E-Boot Loader
Boot loader

What is it ?
Bootloader is the program that reside in specific memory area. This program will program the application program into program area

Why we need bootlaoder ?
Bootloader enable us to re program firmware on the fly with using i2C memory, serial port without any special programming tools make it easily to update firmware in the field via normal communication port

What we need to use bootloader ?
Bootloader quite complex mechanism and you need to set fuse bit programming right in order. If not it will fail

Step to use bootloader

1) Bootloader program need to specify the memory location for the program in MakeFile. By specify BOOTBLOCKSTARTADDRESS = 0x7000 ( For ATMEGA32) and this parameter will use in option
LDSECTION = --section-start=.text=$(BOOTBLOCKSTARTADDRESS)
This option will specify the start address of the code. (See manual for start address) This is another common pitfall because the address in manual is in word ( 2 bytes) Then we need to translate to bytes before we put in makefile

Ex. ATMEGA32 for 2 KWORD block bootloader start address = 0x3800 The value we need to put in makefile is 0x3800 x 2 = 0x7000

1. In program bootloader if you use interrupt vector table. You need to set IVCE, IVSEL in GICR to told the uC that the interrupt vector table have move to new place (bootloader + Vector table )
2. Before go to application. You need to recall the interrupt vector table into the original by reset IVCE and IVSEL
3. Before load the program bootloader. You need to set fuse bits by programmer to control the configuration of bootloader. Which are
  1. Bootloader size BOOTSZ1, BOOTSZ0 specify the size 512 K, 1 K , 2K (word not bytes) This will effect the BOOTBLOCKSTARTADDRESS in 1)
  2. Bootrst to tell uC to use bootloader start address when reset button is pressed
4. After set fuse bit and program the bootloader make sure that the lock bit had been set to protect bootloader overwrite by the application (Bootlock12, Bootlock11)
5. Make sure the serial speed and protocal ( Stop, Start , Parity bits ) match. Between terminal and bootloader
6. To activate bootloader activate condition. ( Pressing SW , Push reset while press i, etc)

Bootloader chip45boot

This boot loader will activate when press i on terminal during press reset the “>” will show on screen. If there are program installed in flash. It will run the program (check 0xFF at 0x0000)
If not they will show “>” and wait for command

f = Flash program download in srec mode
g = Run application
e = Program eeprom

Problems: Cannot program srecord file

STK500boot
After reset, witin 3 seconds if there are no signal from serial. It will go to run application. If there are no application installed, they will loop until found the STK5000 protocal

Problems Cannot program long hex file error !!

Boothex ( Use in E-block)
Problem cannot program at high speed ( 2400 ) Need to modify for Xon/Xoff protocal to avoid buffer overload

Enter boot mode condition
1. No program at 0x0000 ( Read 0xFF )
2. Enter i within period of time
Enter program mode condition
1.There are program at 0x0000 (Checked when press Reset)
2. Press x at bootmode
2
# E_IO Module
 Function Description (API)
io_sw_init ( void)	Initial Switch for use as input IO and initial timer
io_sw_status ( &status) Get the Switch status return in variable first byte
0xAAAA BBBB
A = Status of A
B = Status of B
return value	1 = Press
2 = Release after Press
0 = Nothing happen
3 = Hold more than limited time

Pseudo code
This will help programmer to translate to code in each target CPU
io_sw_init ( void)	I
Initial GPIO as an input and initial timer
io_sw_status ( &status) Pass by reference
Within period of time
Check switch status whether it is
- First Press (Set status)
- Release after press ( Clear status)
- Hold ( still press > limited time)
Put the status in status

Pseudo code
This will help programmer to translate to code in each target CPU
E_7segment_init ( void)
Initial all usage GPIO to output direction
Initial timer interrupt for display refresh

io_7Segment_num ( number)
Convert number to string
Call E_7Segment_str
io_7segment_str (* uint8_t)
      Repeat each timer tick for display
Do Until end of str
   show first character
   move character to left and show next characters
        end
## io_sw
Usage : To get input from SW on E_IO board
Theory of operation: Get the input from two SW in E_IO module. The Switch will connect to GND when pressed. (logic = 0) R internal pull up will enable The module can return the SW mode in many form
Press	Press the SW
Release	Release the SW
Hold	Hold the SW for specifice amount of time
A
# Module Name
Module objective
Describe the module objective, what they do, what is the benefits for this module
Module Requirements
Requirements for this module
Function API
Describe the Function API, Pseudo code for easy port to different platform
Format Return value functioname (parameters)
    Brief description
    Pseudo code
Ex.
void io_7segment_display_str (* uint8_t str )
 Display string pointed by str over 7 Segments ( Ex Hello)
Pseudo Code
Output each characters to Serial characters until end on string (null characters)
UML Diagram
To design the functions, modules usinge the following diagram
- Uses cases
- State transition Matrix
- State diagram
  To create UML use ARGO UML ??? and copy to these section.
  Global Data structure
- Usage of the data structure
- DFD ( If apply)
File location
Source code
Resource usage ( Worksheet)
- Peripheral Ex. Time, Serial
- Port / Pin Usage
- Register usage/ Setting
- Interrupt
- Flash memory
- Data memory
Future enhancement
Future expansion, new features

Include file template (modify for doxygen)

 Include file for	XXXX.c
 Description	File Description
 Written by	Name & Email
 Date	DD/MM/20XX

 Summary for include files
 -------------------------
 Constant variable	X
 Function prototype	-

(move to matrix more calculate)
 Memory	FLASH	XXX Program Size
RAM	XXX
EEPROM	XXX

X = Defined
- = Not Defined

 Update History

 Date	By	Comments
 ----	--	---------

Program Template (modify for doxygen)
Template for program header

 Module	: Module name
 Description	: Module Description
 Original written for	: CPU/Microcontroller
 CPU port/tested	: CPU/Microcontroller
 Hardware use	: IC Chip
 Port use	: Port name / Function
 Memory	FLASH	:	XXX Program Size
RAM	: XXX
EEPROM	: XXX
 Document	: Document describe algorithm
 Written by	: Name / Email
 Date	: DD/MM/20XX

 Update History

 Date	By	Comments
 ----	--	---------

 Platform

FPGA = Hardware IP + RTOS + Driver + Application
   Reconfigure port

E-Block = Hardware E-Block + Software E-block

Resource Usage table
Resource
CPU Port	ATMEGA32
Peripheral	GPIO 10 Ch (E_PA0-7, E_PB1, E_PB2)
	TIMER ( For refresh display)
Program Code
EEPROM	-

Register Setting
E_PA

Template manual
Style in these template
Chapterno number of chapter
Chaptertitle title chapter

Tips to use template
- Always end chapter with page break

How to enter index
How to set//enter chapter
- Goto edit paragraph/styles (click right mouse button)
- select organizer tab
- set next style for style use next
- set style category

How to set/enter toc
- Goto edit index/table
- At index/table tab check outline box and press ... to edit
Map desired style to TOC level