  E-block
Handbook

Vsion	Date	By	Modified
	10/03/2549	Wichai

Eblock Concept

"Building the block and reconnect it as your imagination"

Hardware E-block
Hardware Standard

Standard I/O Port
Socket Upper Left
Socket Upper Right
Socket Lower Left
Socket Lower Right
Socket 4 x 10 pins single row
 Expandable I/O Port
Socket Upper Left x2
Socket Upper Right x2
Socket Lower Left x 2
Socket Lower Right x2
Socket 4 x 10 pins single row
 Hardware module

- CPU
      - AVR
      - PIC
      - ARM
      - DSP
      - PSOC
      - FPGA
- Power supply
      - Regulator
      - Battery
      - Charger
- Input
      - SW
      - Matrix -SW
      - VR
      - CCD
      - Keyboard
      - Real time Clock
      - CAPSense via I2C , SPI)
- Communication
      - USB
      - Serial (RS232, 485)
      - I2C
      - Ethernet
      - Wireless Lan
      - Zigbee
      - Bluetooth
      - Irda
      - UART
      - SPI
      - DTMF ( Telephone)
      - Wiegand
- Measurement
      - Distance (Ultrasonic)
      - Movement (X, Y ) use mouse for sense direction x,y
      - Back EMF
      - Digital Compass
- Output
      - LED
      - Piezo
      - LED DOT MATRIX
      - LCD
      - VGA
- Control
      - Motor DC
      - Servo
      - Stepping Motor
      - Solenoid
- Memory
      - eeprom
      - SDRAM
- Connector
      - Jumper
      - IC Socket jumper
      - Protoboard ???
- Input/ Output
      - Touch Screen
      - SD Card
      - Smart Card
      - RFID
- Sensor
      - Magnetic
      - Temp
      - Light
      - Level/ Tilt
      - Acceletor
      - Location
      - Gyro
      - IR

Software E-block

Software Standard
GNU C
Port mapping table
I/O Function mapping ??
        Interrupt mapping ???
Directory sturcture
Virtual I/O on PC ( ex LCD, LED, SW May use terminal command )

Protocal Standard
Archived library with include file for each module
Function prototypes
Naming convention
        API for each module
 IP block for FPGA
        Text process
      - Decode command
      - Send message
      - XML

- Protocal Stack
      - USB
      - TCP/IP
      - Wifi
      - GPRS
      - Wiegand
      - IR remote
      - I2C
      - SPI
      - CAN
      - RS232
      - RS485
      - Bluetooth
- Application Layer
      - Timer
      - UI
- Algorithm
      - PID
      - Fuzzy logic
      - DSP FTT
      - MP3
      - JPEG
      - MPEG
      - Bitmap
      - Sound CODEC
- INTERFACE
      - LCD
- OS layer
      - Web Service
      - UI
      - RTOS
      - Java ??

Hardware E-Block issues
I/O board if design to left side (I/O port) or right side( Communication/ Int) cannot
 swap right/left.
        Board which use signals lines need to take off that signal lines. (Not bypass) except some communication ex. I2C
Interrupt handling

Software E-Block issues
Global variable communicate
Interrupt handling
Duplicate naming convention for function name variable
Naming convention
Prefix with module name ??
Ex LED_xxxx
        RTC_xxxx
Module Catalog
Collect all catalog for modules and implementation sample
Module
Hardware block
Hardware circuit diagram
PCB (if any)
Standard connector
Used connector
Software block
Include file
Source code file
Object
          - Attributes (values)
          - Data structure (if apply)
          - Behaviors ( function)
          - State (state values)
        Function
Set_xxx Initial values
Get_xxx Get values

Documentation using doxygen, State diageam UML diagram ??
Module description
State diagram
Attributes, function description
Algorithm, resposibility
Data structure description
Port / Service use matri
Hardware components
Theory of operation

Naming conventions
Global variable	g_XXXX
Procedure name	Module name_active_name_procedure_name

wef

E-block specification
Hardware Specification for CPU Board

Hardware Specification for E_IO Board

Hardware physical for protoboard

Connector Standard

Upper Right Connector : Communication
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For ATMEGA32 and ATMEGA8

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	VCC	VCC (5,38,17)	VCC (4,6)
2	GND	GND(6,18,39)	GND(3,5)
3	SCL/ E_PORTD0	PC0(19)	PC5(28)* JP1
4	SDA/ E_PORTD1	PC1(20)	PC4(27)* JP2
5	RX/ E_PORTD2	PD0(9)** JP3	PD0(30) *
6	TX/ E_PORTD3	PD1(10)* JP4	PD1(31) *
7	INT0/ E_PORTD4	PD2(11)	PD2(32)* JP3
8	ICP/ E_PORTD5	PD6(15)* JP1	PB0(12)* JP4
9	TIMER1/ E_PORTD6	PD5(14)/OC1A	PB1(13)* JP5
10	TIMER2/ E_PORTD7	PD4(13)/OC1B	PB2(14)* JP6

Lower Right connector : Anaglog Input
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files :

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	AVCC	AVCC(27)	AVCC(18)
2	AREF	AREF(29)	AREF(20)
3	ADC_1/E_PORTC0	PA0(37)	PC0(23)
4	ADC_2/E_PORTC1	PA1(36)	PC1(24)
5	ADC_3/E_PORTC2	PA2(35)	PC2(25)
6	ADC_4/E_PORTC3	PA3(34)	PC3(26)
7	ADC_5/E_PORTC4	PA4(33)	PC4(27)*
8	ADC_6/E_PORTC5	PA5(32)	PC5(28)*
9	ADC_7/E_PORTC6	PA6(31)	ADC6(19)
10	ADC_8/E_PORTC7	PA7(30)	ADC7(22)

Upper Left connector : Digital O/P / SPI
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For ATMEGA32 and ATMEGA8

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	VCC	VCC(5,17,38)	VCC (4,6)
2	GND	GND(6,18,39)	GND(3,5)
3	E_PORTA0	PB0(40)	PD4(2)
4	E_PORTA1	PB1(41)	PD5(9)
5	E_PORTA2	PB2(42)	PD6(10)
6	E_PORTA3	PB3 (43)	PD7(11)
7	E_PORTA4 /SS	PB4(44)	PD2(32)*
8	E_PORTA5 / MOSI	PB5(1)	PD3(1)*
9	E_PORTA6/ MISO	PB6(2)
10	E_PORTA7/ SCK	PB7(3)

Lower Left connector : Digital I/P
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For ATMEGA32 and ATMEGA8

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	TIMER0	PD7(16) JP2	PB3(15)* JP7
2	INT1	PD3(12)	PD3(1)* JP8
3	E_PORTB0	PC2(21)	PB0(12)*
4	E_PORTB1	PC3(22)	PB1(13)*
5	E_PORTB2	PC4(23)	PB2(14)*
6	E_PORTB3	PC5(24)	PB3(15)*
7	E_PORTB4	PC6(25)	PB4(44)
8	E_PORTB5	PC7(26)	PB5(1) / ( use for mode switch)
9	E_PORTB6	PD7(16) JP2
10	E_PORTB7/ICP	PD6(15) * JP1

* Selectable by Jumprt right left
** Jumper select for using TX/RX or PortD

Upper Right connector : Communications
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	VCC (5V)	Not use (3.3 V)*
2	GND	GND
3	SCL/ E_PORTD0	P0.2
4	SDA/ E_PORTD1	P0.3
5	RX/ E_PORTD2	P0.9
6	TX/ E_PORTD3	P0.8
7	INT0/ E_PORTD4	P0.16
8	ICP/ E_PORTD5	P0.11
9	TIMER1/ E_PORTD6	P0.12
10	TIMER2/ E_PORTD7	P0.13

Lower Right connector : Analog Input
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	Exint2/ ADC (AVCC for Mega)	P0.15
2	D/A (AREF for Mega)	P0.25
3	ADC_1/E_PORTC0	P0.27
4	ADC_2/E_PORTC1	P0.28
5	ADC_3/E_PORTC2	P0.29
6	ADC_4/E_PORTC3	P0.30
7	ADC_5/E_PORTC4	P0.26
8	ADC_6/E_PORTC5	P0.4
9	ADC_7/E_PORTC6	P0.5
10	ADC_8/E_PORTC7	P0.6

Upper Left connector : Digital O/P / SPI
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	VCC (5V)	Not use ( use 3.3 V) *
2	GND	GND
3	E_PORTA0	P1.23
4	E_PORTA1	P0.31
5	E_PORTA2	P0.23
6	E_PORTA3	P0.21
7	E_PORTA4 /SS	P0.20
8	E_PORTA5/MOSI	P0.19
9	E_PORTA6/ MISO	P0.18
10	E_PORTA7/SCK	P0.17

Lower Left connector : Digital I/P
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	TIMER0	P0.22
2	INT1	P0.14
3	E_PORTB0	P1.16
4	E_PORTB1	P1.17
5	E_PORTB2	P1.18
6	E_PORTB3	P1.19
7	E_PORTB4	P1.20
8	E_PORTB5	P1.21
9	E_PORTB6	P1.22
10	E_PORTB7/ICP	P0.10

Center Left connector : Vcc
Connector 1x 2 pins Male
Part number :
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	Vcc 3.3	Vdd
2	GND	Gnd

Center right connector : Vcc
Connector 1x2 pins Male
Part number :
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	Vcc 3.3	Vdd
2	GND	Gnd

JTAG
Connector 2x 10 pins Male
Part number :
Spec files : For LPC2138 (ARM7)

Pin	Signal	LPC2138 (ARM7)
1	3V3	3V3
2	3V3	3V3
3	nTRST	P1.31
4	Gnd	Gnd
5	TDI	P1.28
6	Gnd	Gnd
7	TMS	P1.30
8	Gnd	Gnd
9	TCK	P1.29
10	Gnd	Gnd
11	RTCK	P1.26
12	Gnd	Gnd
13	TDO	P1.27
14	Gnd	Gnd
15	RST#	RST#
16	Gnd	Gnd
17	NC	NC
18	Gnd	Gnd
19	NC	NC
20	Gnd	Gnd

Note
LPC2138 use 3.3 not 5.0 V The power for 3.3 is extra socket between upper and lower connectors on both side

# Future expand
E-block can expandable to 80 pins by connecting 2 standard size boards in vertical this make up all I/O become 80 pins. Because of this topology. We can still use old moudles for 40 pins CPU

Software Specification

Include file template (modify for doxygen)

 Include file for	XXXX.c
 Description	File Description
 Written by	Name & Email
 Date	DD/MM/20XX

 Summary for include files
 -------------------------
 Constant variable	X
 Function prototype	-

(move to matrix more calculate)
 Memory	FLASH	XXX Program Size
RAM	XXX
EEPROM	XXX

X = Defined
- = Not Defined

 Update History

 Date	By	Comments
 ----	--	---------

Program Template (modify for doxygen)
Template for program header

 Module	: Module name
 Description	: Module Description
 Original written for	: CPU/Microcontroller
 CPU port/tested	: CPU/Microcontroller
 Hardware use	: IC Chip
 Port use	: Port name / Function
 Memory	FLASH	:	XXX Program Size
RAM	: XXX
EEPROM	: XXX
 Document	: Document describe algorithm
 Written by	: Name / Email
 Date	: DD/MM/20XX

 Update History

 Date	By	Comments
 ----	--	---------

 Platform

FPGA = Hardware IP + RTOS + Driver + Application
   Reconfigure port

E-Block = Hardware E-Block + Software E-block

Issues

Software
How to mapping for different Port and Port number on the same connector
Ex Connect have PortA2, PortB5 How to program like it the same virtual Port
( E_PORTB1, E_PORTB2)

Hardware

Connector
Need jumper for communcation port and standard I/O port especially small pin microcontroller

Boot loader

What is it ?
Bootloader is the program that reside in specific memory area. This program will program the application program into program area

Why we need bootlaoder ?
Bootloader enable us to re program firmware on the fly with using i2C memory, serial port without any special programming tools make it easily to update firmware in the field via normal communication port

What we need to use bootloader ?
Bootloader quite complex mechanism and you need to set fuse bit programming right in order. If not it will fail

Step to use bootloader

1) Bootloader program need to specify the memory location for the program in MakeFile. By specify BOOTBLOCKSTARTADDRESS = 0x7000 ( For ATMEGA32) and this parameter will use in option
LDSECTION = --section-start=.text=$(BOOTBLOCKSTARTADDRESS)
This option will specify the start address of the code. (See manual for start address) This is another common pitfall because the address in manual is in word ( 2 bytes) Then we need to translate to bytes before we put in makefile

Ex. ATMEGA32 for 2 KWORD block bootloader start address = 0x3800 The value we need to put in makefile is 0x3800 x 2 = 0x7000

1. In program bootloader if you use interrupt vector table. You need to set IVCE, IVSEL in GICR to told the uC that the interrupt vector table have move to new place (bootloader + Vector table )
2. Before go to application. You need to recall the interrupt vector table into the original by reset IVCE and IVSEL
3. Before load the program bootloader. You need to set fuse bits by programmer to control the configuration of bootloader. Which are
  1. Bootloader size BOOTSZ1, BOOTSZ0 specify the size 512 K, 1 K , 2K (word not bytes) This will effect the BOOTBLOCKSTARTADDRESS in 1)
  2. Bootrst to tell uC to use bootloader start address when reset button is pressed
4. After set fuse bit and program the bootloader make sure that the lock bit had been set to protect bootloader overwrite by the application (Bootlock12, Bootlock11)
5. Make sure the serial speed and protocal ( Stop, Start , Parity bits ) match. Between terminal and bootloader
6. To activate bootloader activate condition. ( Pressing SW , Push reset while press i, etc)

Bootloader chip45boot

This boot loader will activate when press i on terminal during press reset the “>” will show on screen. If there are program installed in flash. It will run the program (check 0xFF at 0x0000)
If not they will show “>” and wait for command

f = Flash program download in srec mode
g = Run application
e = Program eeprom

Problems: Cannot program srecord file

STK500boot
After reset, witin 3 seconds if there are no signal from serial. It will go to run application. If there are no application installed, they will loop until found the STK5000 protocal

Problems Cannot program long hex file error !!

Boothex ( Use in E-block)
Problem cannot program at high speed ( 2400 ) Need to modify for Xon/Xoff protocal to avoid buffer overload

Enter boot mode condition
1. No program at 0x0000 ( Read 0xFF )
2. Enter i within period of time
Enter program mode condition
      1 There are program at 0x0000 (Checked when press Reset)
      2 Press x at bootmode

Directory Structure
E-block\hw
     \Hardware module name
\Circuit diagram	Schematics of H/W block
\PCB	PCB for hardware module
\document	Document explain Circuit\
\sw
    \CPU CPU name Ex. ARM, AVR
\Module Name (*.c *.h)
\document	Document explain library

Please note that one Hardware module may link to many Software module. Ex. E_IO pcb can call routine for 7 segments display, IR Switch press

# E-block product development process
This topic explain all process to develope embedded system. If you want develop only E-block libray/ module go to E-block module development

Product Concept
Product specification
Product scneario example (optional)
Product specification
High level design context diagram
Detailed product specification
Design phase ( if apply, to make it smaller and manageable)
Test case
Test script
High level design ( depend on users' choice. Goal is to make design clear to others)
UML
Data Flow Diagram
State transition matrix)
State table

Hardware /Software partition
This step divide the product implementation in Hardware side and Software side. Designer will need to identify part implements by Hardware or Software. Because some part you can use already build IC chip or implement by S/W into uC For ex. Tcp/IP stack can use both S/W or H/W to implement

Hardware Design
1. Divide in module
2. Interface Design between module
3. Document theory of operation and interface design
4. Select from available E-block module or create the new one. If there are no available E-block in the port. You can create the new one. (Go to E-block module development for information how to create E-block H/W module)
5. Slove the conflict of port ( if any)
6. Test and debug module accroding to spec.
7. Check in all document and diagram
Software design
1. Document Theory of operation
2. Resource usage, interrupt and register setting
3. Function description (API)
4. State diagram & UML
5. Psedo code for translate to different CPU architecture
6. Create library in \Eblock\SW\CPU\Modulename directory. There are at least 2 files source code (.c) files and header file for include (*.h) under module name directory. ( or library *.a to avoid module overwrite)
Test and debug module accroding to spec.
Check in for each library

Note that E-block SW and E-block HW may not match. For example E_IO h/w block may use IR Control, Sound, 7 Segments display module.

Intergration Develope
1. Document main logic to glue all e-block together
2. Set include file directory in Makefile point to Eblock files
3. Add source code into project files or library
4. Writng main logic code
Testing
Follow test script for integration test

End project
Check in all project documets
Prepare for bug feedback channel
Publish to web

# E-block module development
To develop new E-block module. We can divided into two parts E-block H/W and E-block SW
E-block Hardware Design
For Hardware design, we can classified two groups of E-block HW
CPU to create E-block for CPU we need to follow these guidelines.
USE male connectors for both side
Schematic design
PCB design ( or use protoboard)
Test and debug module accroding to spec
Document theory of operation and specification, usage
Check in all document and diagram

      2)	Peripheral
Select whether connect right side or left side depend on characteristic of peripheral
Define port use
Bypass all the signal bus do not use
Connector and jumper may be used if you want to switch from one side to another side
Slove the conflict of port ( if any)
Schematic design
PCB design ( or use protoboard)
Test and debug module accroding to spec.
Document theory of operation, apply application sample, specification, usage
Check in all documents and diagram
Document need
Schematic Design
PCB Design
Theory of operation, Spec
Software design
1. Document theory of operation apply application sample, specification, usage
2. Resource usage, interrupt and register setting
3. State diagram & UML
4. Psedo code for translate to different CPU architecture
5. Define API
6. Create library in \Eblock\SW\CPU\Modulename directory. There are at least 2 files source code (.c) files and header file for include (*.h) under module name directory. ( or library *.a to avoid module overwrite)
Test and debug module accroding to spec.
Check in all documents for each library
Document need
Source code
Theory of operaion, Spec
UML, State diagram (optional)

Note that E-block SW and E-block HW may not match. For example E_IO h/w block may use IR Control, Sound, 7 Segments display module.

# E-block roadmap
Expandable to 80 pins for complex task
CPLD for reconfiguration pins
FPGA for handling device IO
Multi processor to share load and make it more independent module (M2M protocal)
Using E_smartIO ATMEGA8 to control various protocal and convert to I2C or SPI
E-block script
labview interface
# E-block Application
E-bot for robot builder
E-pro E-block for professional more efficient commercial product
E-game E-block to create games like arcade game

# E-block Software module
SW Module	HW Module
io_7segment.c,.h	E_IO
io_piezo.c,.h	E_IO
io_sw.c,.h	E_IO
io_ir.c,.h	E_IO
io_uart,.h	E_Mega32
io_i2c,.h	E_Mega32
io_eeprom,.h	E_Mega32
io_adc.c,.h	E_Mega32
io_keyboard,.h	E_XXX

## io_7segment
Usage : To display Number up to10 digits. The characters can shown with limited characters. Ex We can not show these characters nicely z,m,w when display more than 2 characters the display will scroll.
Theory of operation: These 2 digits share the same pin for each segments and seperate each digit with common cathode (-) To display both characters simultaneously, we need to fast switch betweeen two digits. If it's fast enough, users will not see it flicker. To scroll message just move 1 digits to the left and display next digits to replace the old ones
Resource Usage table
Resource
CPU Port	ATMEGA32
Peripheral	GPIO 10 Ch (E_PA0-7, E_PB1, E_PB2)
	TIMER ( For refresh display)
Program Code
EEPROM	-

Register Setting
E_PA

 Function Description (API)
E_7segment_init ( void)	Initial 7 Segments. This routine will set register setting to initial GPIO direction to be output
E_7Segment_num ( number) To display number in decimal number
E_7segment_str (* uint8_t) Display string over 7 Segments ( Ex Hello)
State diagram &UML (Future)

Pseudo code
This will help programmer to translate to code in each target CPU
E_7segment_init ( void)
Initial all usage GPIO to output direction
Initial timer interrupt for display refresh

io_7Segment_num ( number)
Convert number to string
Call E_7Segment_str
io_7segment_str (* uint8_t)
      Repeat each timer tick for display
Do Until end of str
   show first character
   move character to left and show next characters
        end

Future enhancement
io_7Segment_float ( float) Floating point

## io_sw
Usage : To get input from SW on E_IO board
Theory of operation: Get the input from two SW in E_IO module. The Switch will connect to GND when pressed. (logic = 0) R internal pull up will enable The module can return the SW mode in many form
Press	Press the SW
Release	Release the SW
Hold	Hold the SW for specifice amount of time
Resource Usage table
Resource
CPU Port	ATMEGA32
Peripheral	GPIO 2 Ch ( E_PB0, E_PB3)
	TIMER ( Use with 7 Segments)
Program Code
EEPROM	-

Register Setting

 Function Description (API)
io_sw_init ( void)	Initial Switch for use as input IO and initial timer
io_sw_status ( &status) Get the Switch status return in variable first byte
0xAAAA BBBB
A = Status of A
B = Status of B
return value	1 = Press
2 = Release after Press
0 = Nothing happen
3 = Hold more than limited time

State diagram &UML (Future)

Pseudo code
This will help programmer to translate to code in each target CPU
io_sw_init ( void)	I
Initial GPIO as an input and initial timer
io_sw_status ( &status) Pass by reference
Within period of time
Check switch status whether it is
- First Press (Set status)
- Release after press ( Clear status)
- Hold ( still press > limited time)
Put the status in status

# E-block OpenCourseware
Objective : Give everyone access to learing material. Develope courseware with objective shorter learning curves with standard protocal to make learner learn faster and deeper until can develope their own products like professional
Mission
Transfer professional knowledge to novice become professional less time with effective project hand on experience

Concepte behing the learning curves.
1. Challenge users interest by attractive project development
2. Users learn by doing project through example gain experience from professional
3. Users gather their own ideas with using basic block from what they learn
4. Intergrate their ideas into composing block to generate new product concepts
5. exapand what they learned and give it back to community

Incubator model (Baby model)
1. Feed everything ( Learn from project, example )
2. Learn to feed yourself ( Modify example, projects)
3. Learn to find food ( Gathering E-block for new projects)
4. Learn to find money to buy food ( Create new E-block for new application area)