E-block
H/W
Module Spec.

Vsion	Date	By	Modified
	10/03/2549	Wichai

0
# Guidelines for the template
Use this template to document the new HW template. Chapter 1 is the index for all HW block. Start from chapter 2 is each HW block spec which compose of the following items. Appendix A is the chapter template. To use template copy Appendix A to your new chapter. And fill in the template.
- Block Objective
- Theory of operation for this module
- Files location
- Pins diagram
- Schematics description
- Resource Usage ( Worksheet)
- Future enhancement
  For new block development, update chapter 1 to add new block.
1
# HW Block catalog
This chapter collects all the HW blocks which had been developed.
E-block Hardware block
HW block	Description
E_IO	I/O for E-block
E_Mega32	ATMEGA32 Module
E_SD card	SD Card
E_Serial_camera	Serial camera interface
E_vga

2
# E-Mega32 H/W Module

Spec files : For LPC2138 (ARM7)

Connector Standard

Upper Right Connector : Communication
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For ATMEGA32 and ATMEGA8

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	VCC	VCC (5,38,17)	VCC (4,6)
2	GND	GND(6,18,39)	GND(3,5)
3	SCL/ E_PORTD0	PC0(19)	PC5(28)* JP1
4	SDA/ E_PORTD1	PC1(20)	PC4(27)* JP2
5	RX/ E_PORTD2	PD0(9)** JP3	PD0(30) *
6	TX/ E_PORTD3	PD1(10)* JP4	PD1(31) *
7	INT0/ E_PORTD4	PD2(11)	PD2(32)* JP3
8	ICP/ E_PORTD5	PD6(15)* JP1	PB0(12)* JP4
9	TIMER1/ E_PORTD6	PD5(14)/OC1A	PB1(13)* JP5
10	TIMER2/ E_PORTD7	PD4(13)/OC1B	PB2(14)* JP6

Lower Right connector : Anaglog Input
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files :

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	AVCC	AVCC(27)	AVCC(18)
2	AREF	AREF(29)	AREF(20)
3	ADC_1/E_PORTC0	PA0(37)	PC0(23)
4	ADC_2/E_PORTC1	PA1(36)	PC1(24)
5	ADC_3/E_PORTC2	PA2(35)	PC2(25)
6	ADC_4/E_PORTC3	PA3(34)	PC3(26)
7	ADC_5/E_PORTC4	PA4(33)	PC4(27)*
8	ADC_6/E_PORTC5	PA5(32)	PC5(28)*
9	ADC_7/E_PORTC6	PA6(31)	ADC6(19)
10	ADC_8/E_PORTC7	PA7(30)	ADC7(22)

Upper Left connector : Digital O/P / SPI
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For ATMEGA32 and ATMEGA8

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	VCC	VCC(5,17,38)	VCC (4,6)
2	GND	GND(6,18,39)	GND(3,5)
3	E_PORTA0	PB0(40)	PD4(2)
4	E_PORTA1	PB1(41)	PD5(9)
5	E_PORTA2	PB2(42)	PD6(10)
6	E_PORTA3	PB3 (43)	PD7(11)
7	E_PORTA4 /SS	PB4(44)	PD2(32)*
8	E_PORTA5 / MOSI	PB5(1)	PD3(1)*
9	E_PORTA6/ MISO	PB6(2)
10	E_PORTA7/ SCK	PB7(3)

Lower Left connector : Digital I/P
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For ATMEGA32 and ATMEGA8

Port	E_port Name	ATMEGA32(TQFP)	ATMEG8(TQFP)
1	TIMER0	PD7(16) JP2	PB3(15)* JP7
2	INT1	PD3(12)	PD3(1)* JP8
3	E_PORTB0	PC2(21)	PB0(12)*
4	E_PORTB1	PC3(22)	PB1(13)*
5	E_PORTB2	PC4(23)	PB2(14)*
6	E_PORTB3	PC5(24)	PB3(15)*
7	E_PORTB4	PC6(25)	PB4(44)
8	E_PORTB5	PC7(26)	PB5(1) / ( use for mode switch)
9	E_PORTB6	PD7(16) JP2
10	E_PORTB7/ICP	PD6(15) * JP1

* Selectable by Jumprt right left
** Jumper select for using TX/RX or PortD

Upper Right connector : Communications
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	VCC (5V)	Not use (3.3 V)*
2	GND	GND
3	SCL/ E_PORTD0	P0.2
4	SDA/ E_PORTD1	P0.3
5	RX/ E_PORTD2	P0.9
6	TX/ E_PORTD3	P0.8
7	INT0/ E_PORTD4	P0.16
8	ICP/ E_PORTD5	P0.11
9	TIMER1/ E_PORTD6	P0.12
10	TIMER2/ E_PORTD7	P0.13

Lower Right connector : Analog Input
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	Exint2/ ADC (AVCC for Mega)	P0.15
2	D/A (AREF for Mega)	P0.25
3	ADC_1/E_PORTC0	P0.27
4	ADC_2/E_PORTC1	P0.28
5	ADC_3/E_PORTC2	P0.29
6	ADC_4/E_PORTC3	P0.30
7	ADC_5/E_PORTC4	P0.26
8	ADC_6/E_PORTC5	P0.4
9	ADC_7/E_PORTC6	P0.5
10	ADC_8/E_PORTC7	P0.6

Upper Left connector : Digital O/P / SPI
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	VCC (5V)	Not use ( use 3.3 V) *
2	GND	GND
3	E_PORTA0	P1.23
4	E_PORTA1	P0.31
5	E_PORTA2	P0.23
6	E_PORTA3	P0.21
7	E_PORTA4 /SS	P0.20
8	E_PORTA5/MOSI	P0.19
9	E_PORTA6/ MISO	P0.18
10	E_PORTA7/SCK	P0.17

Lower Left connector : Digital I/P
Connector 1x 10 pins Male
Part number : 2211R-10G-LP-F1
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	TIMER0	P0.22
2	INT1	P0.14
3	E_PORTB0	P1.16
4	E_PORTB1	P1.17
5	E_PORTB2	P1.18
6	E_PORTB3	P1.19
7	E_PORTB4	P1.20
8	E_PORTB5	P1.21
9	E_PORTB6	P1.22
10	E_PORTB7/ICP	P0.10

Center Left connector : Vcc
Connector 1x 2 pins Male
Part number :
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	Vcc 3.3	Vdd
2	GND	Gnd

Center right connector : Vcc
Connector 1x2 pins Male
Part number :
Spec files : For LPC2138 (ARM7)

Port	E_port Name	LPC2138 (ARM7)
1	Vcc 3.3	Vdd
2	GND	Gnd

JTAG
Connector 2x 10 pins Male
Part number :
Pin	Signal	LPC2138 (ARM7)
1	3V3	3V3
2	3V3	3V3
3	nTRST	P1.31
4	Gnd	Gnd
5	TDI	P1.28
6	Gnd	Gnd
7	TMS	P1.30
8	Gnd	Gnd
9	TCK	P1.29
10	Gnd	Gnd
11	RTCK	P1.26
12	Gnd	Gnd
13	TDO	P1.27
14	Gnd	Gnd
15	RST#	RST#
16	Gnd	Gnd
17	NC	NC
18	Gnd	Gnd
19	NC	NC
20	Gnd	Gnd

Note
LPC2138 use 3.3 not 5.0 V The power for 3.3 is extra socket between upper and lower connectors on both side

Future expand
E-block can expandable to 80 pins by connecting 2 standard size boards in vertical this make up all I/O become 80 pins. Because of this topology. We can still use old moudles for 40 pins CPU

3
# E-IO Block
Usage : To display Number up to10 digits. The characters can shown with limited characters. Ex We can not show these characters nicely z,m,w when display more than 2 characters the display will scroll.
Theory of operation: These 2 digits share the same pin for each segments and seperate each digit with common cathode (-) To display both characters simultaneously, we need to fast switch betweeen two digits. If it's fast enough, users will not see it flicker. To scroll message just move 1 digits to the left and display next digits to replace the old ones

A
# H/W Block template
Block Objective
What is this block objective
Block requirement
What need to be developed.
Theory of Operation
Describe the technology use in the module Ex. SD_ Card, LAN
Files Location
- Schematics location
- PCB location
BOM
- Parts number and quantity
- Price
Pin diagram
How the pins are connected according to E-block standard. Which pins have been used.
Jumper select (if apply)
Schematics Description
Explain the operation of circuit
H/W Resource usage ( Worksheet)
- Peripheral Ex. Timer, Serial
- I/O Port / Pin Usage
- Register usage/ Setting
  Relate Software module
  To show which software module relate to this HW block
Future enhancement
Potential future expand

Template manual
Style in these template
Chapterno number of chapter
Chaptertitle title chapter

Tips to use template
Always end chapter with page break

How to enter index
How to set//enter chapter
- Goto edit paragraph/styles (click right mouse button)
- select organizer tab
- set next style for style use next
- set style category

How to set/enter toc
- Goto edit index/table
- At index/table tab check outline box and press ... to edit
Map desired style to TOC level