Security door
using RFID
product
Specification.

1
# Product requirements
To show the product requirement in term of
Overall product description
H/W requirements Ex. Need SD card, LAN
S/W requirements Ex. Need support TCP/IP, IR protocal
User interface requirement ex. Graphic, text
Packaging requirement Ex. Size, Material
Product concepts
อุปกรณ์ควบคุมการเปิดปิดประตูโดยใช้เทคโนโลยี RFID ในการระบุตัวบุคคลเพื่ออนุญาติหรือไม่อนุญาติให้เข้าภายในอาคาร
Product description
- สามารถตรวจสอบได้ว่ามี RFID card ที่นำมา stamp เหมือนหรือต่างกับ ข้อมูล RFID card ที่เก็บอยู่
- สามารถเก็บ รหัส RFID card เข้าสู่ระบบได้
- สามารถลบ รหัส RFID card ออกจากระบบได้
- สามารถเก็บเวลาที่มีการนำ RFID card มาทำการ stampได้
- สามารถใช้ RFID เชื่อมต่อแบบ Wiegand interface ได้
- สามารถใช้รหัสผ่านในการเปิดประตู แทน RFID card ได้
- สามารถเก็บข้อมูลลงใน SD/MMC Card ได้
- สามารถแสดงผลผ่าน GLCD ได้
- สามารถนับเวลาได้แม้จะไม่มีการจ่ายไฟให้กับระบบ
H/W requirements (SYSTEM REQUIREMENT FEATURES)
No	Requirements
HW-1	Use ARM7 as the core development
HW-2	Support Wiegand interface for LF 125 MHZ and MF (13.5 Mhz)
HW-3	Use keypad for the input
HW-4	Interface to 220 V device for control doors
HW-5	Menu select on LCD for operation
HW-6	Can save data in SD card
HW-7	Can save time when power off and on again

S/W requirements
No	Requirements
SW-1	Input password and control using keypad
SW-2	Read and compare RFID card with the Database
SW-3	Add , Delete RFID Card from the database
SW-4	Output control to relay to control 220 V device
SW-5	Can show graphic icons
SW-6	Can show character in text mode
SW-7	Menu driven interface
SW-8	Read /Write data to SD card
SW-9	Can save time
SW-10	Can set time

2
# Module Partition
This chapter partition project into block. Both HW block and SW block an check whether block available or need to new design or expand current block. (Use to show for who do what and task done)
E-block Software for ARM module
Need SW Module	Available	Create new
E_ARM7_Keypad	No	Yes
E_ARM7_TIME	No	Yes
E_ARM7_SPI	No	Yes
E_ARM7_GLCD	No	Yes
E_ARM7_RFID	No	Yes
E_ARM7_Relay	No	Yes
E_ARM7_SD/MMC	No	Yes

E-block Hardware module
Need HW block	Available	Create new
E_ARM7	Yes	No
E_Keypad	Yes	No
E_GLCD	No	Yes
E_RFID	No	Yes
E_SD/MMC	No	Yes
E_Relay	Yes	No

E-block Hardware module requirement
HW block	Need Features	Requirement Mapping
E_ARM7	E_ARM 7 ( E-block CPU using ARM7 LPC2138) / Map to E-block pin / Serial port and JTAG port to program / Battery 3 V connect to RTC	HW-1 / HW-7
E_RFID	E_RFID Wiegand RFID (125 kHz) / Output in Wiegand interface / Regulate 5 V from 12 V ( Reduce power supply)	HW-2
E_MATRIX	E_MATRIX Key pad 12 key (4 x 3) / Support 12 key press / IO need for Rows and column	HW-3
E_Relay	E_Relay ( ส่วนจำลอง การควบคุม เปิด-ปิด ประตู ) / IO need for control relay	HW-4
E_GLCD	E_GLCD ( ET-NOKIA LCD 5110 ) / Backlight for LCD / SPI interface	HW-5
E_SD/MMC	E_SD/MMC Reader (ET-MINI SD/MMC) / SPI interface / SD/MMC socket	HW-6

E-block Software module requirement
SW block	Need Features	Requirement Mapping
E_ARM7_Keypad	Keypad Controller / Can get pressed key from keypad ( 12 key)	SW-1
E_ARM7_RFID	RFID Reader Controller / Can get data from RFID card	SW-2
E_ARM7_Relay	Relay Controller / Can receive input and simulate door open	SW-4
E_ARM7_GLCD	Graphic LCD Controller / Can show picture / Can convert character to show on LCD	SW-5 / SW-6 / SW-7
E_ARM7_SD/MMC	SD/MMC Reader controller / Can load data / Can save data	SW-8
E_ARM7	Read RFID using interrupt / Add , Delete RFID Card from the database	SW-3
E_ARM7_TIME	Save /Set time using RTC	SW-9 / SW-10
E_ARM7_SPI	Interface with SD and GLCD via SPI

3
# Module Integration
This chapter explain how to do module integration both H/W and S/W module

H/W integration

S/W integration
file	SercurityDoorFlowChart.jpg
SercurityDoorFlowChart.pdf
4
# Testing
Testing environment
Specify testing environment use in this project
There are tests for module and integration test for whole project.
Module testing refer to each module testing work sheet.
Integration testing map by translate requirement to test case, specify test expectation and test results

From requirement table map to test case

Requirement	Test cases	Expect results	Results
HW-1	1.1 Load program into E_ARM / 1.2 Run program from E_ARM	Load and run program properly
HW-2
HW-3
HW-4
HW-5
HW-6
HW-7
SW-1
SW-2
SW-3
SW-4
SW-5
SW-6
SW-7
SW-8
SW-9
SW-10

5
# Wrap up
This chapter is check list for project wrap up to make sure that all documents and files had been updated properly

Tasks	Status
Update E_Block_HWSpec
Update E_Block_SWSpec
Project document
Put all source code in repository
Put all schematics in repository
Put all PCB in repository
Update Web and E-block catalog
Provide bug report form